## Slide 1: Tier 3 gasoline – A wolf in sheep’s clothing?
George Hoekstra
OPIS Fuels and Octane Forum Oct. 24, 2019
Notes: Five years ago, in October of 2014, I was in a meeting with a refiner who was very interested in Tier 3 gasoline, which was a hot topic back then. We were collaborating in a research project to address some weak links in Tier 3 technology. The project included pilot plant testing and commercial field testing focused on gasoline desulfurization. Now, five years later, I have been asked to talk today on this topic: Tier 3 gasoline – a wolf in sheep’s clothing? And I thank Tom Kloza for creating this title. It is a great title because my theme today is there is much more to Tier 3 than meets the eye.

## Slide 2: Tier 3 gasoline
Mandates 10 ppm average annual sulfur limit
Enacted in 2014
Phased-in 2017-2020
2018 average sulfur was 21 ppm
2019 average will still be way over 10 ppm
A lot of work remains
Notes: The Tier 3 gasoline standard mandates a 10 ppm average annual sulfur limit on gasoline in the United States. It was enacted in 2014 and phased in from 2017 to 2020. In 2018, the average sulfur was 21 ppm, and we predict the 2019 average will still be way over 10 ppm. A lot of work remains to meet the goal. During our 3-year research project, I was tracking the average sulfur in gasoline in the United States.

## Slide 3: Sulfur reduction toward 10 ppm has been slow
Chart: US average ppm sulfur in gasoline
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
Sulfur VWA | 31.49 | 30.72 | 28.83 | 26.61 | 24.51 | 23.85 | 21.2 | 20.5 | 0 | 10 | 10
Gap
Updated June 24, 2019
Notes: Sulfur reduction toward 10 ppm has been slow. Starting from 31 ppm in 2011, the annual average sulfur crept down to 21 in 2017 and 18, meaning there’s an 11 ppm gap still to be filled. And those 11 ppm are in the red zone, meaning they’re much harder get than those we got so far.

## Slide 4: Tier 3 gasoline
Is the industry ready?
What’s the problem?
What’s going to happen?
Notes: Is the industry ready?
What’s the problem?
And What’s going to happen?

## Slide 5: Tier 3 gasoline
Is the industry ready? No.
What’s the problem?
What’s going to happen?
Notes: Is the industry ready? I say no. This is a minority opinion. In fact, for a long time, the industry consensus has been that Tier 3 is a done deal. And in 2nd quarter earnings conference calls in August, top refining executives were asked about it, and they said yes, the industry is ready. There are several reasons why I disagree. To explain one of those reasons, we must focus on a specific part of a US refinery.

## Slide 6
Fluid cat cracking (FCC) process train
Thanks to John Jechura
Colorado School of Mines
for refinery flowchart
Notes: The fluid catalytic cracking (FCC) process train is highlighted here in green. Starting at the left, the first green block is the feed hydrotreater which pretreats low value, high sulfur, heavy oil, then the second green block, the fluid cat cracker, or FCC, cracks it to gasoline which is then desulfurized in the third green block, the gasoline desulfurizer. The product, FCC gasoline, is the largest component of the US gasoline pool. It is also the source of almost all the sulfur in the pool. The key to meeting the Tier 3 spec is to reduce the sulfur in this FCC gasoline stream. And the weak link is in this train.

## Slide 7
Yellow refinery – no gasoline desulfurizer
Notes: This train, shown in yellow has no gasoline desulfurizer. I will refer to this as a yellow refinery.

## Slide 8
Red refinery – no FCC feed hydrotreater
Notes: And this FCC train has no feed hydrotreater. I call this a red refinery.

## Slide 9
Three categories of FCC refinery | 
 | Complete FCC train
 | No gasoline desulfurizer
 | No feed hydrotreater
Notes: So consider three categories of FCC refineries: green, with a complete train, yellow, with no gasoline desulfurizer, and red, with no feed hydrotreater. The point is that green refineries have a huge advantage for making Tier 3 gasoline. In fact, wherever in the world 10 ppm sulfur gasoline is made today, like Europe and California, refineries fall mostly in the green category. The United States will now we be relying heavily on yellow and red refineries. They will have little margin for error. Red refineries especially, have a big disadvantage. They lack the FCC feed hydrotreater which is a high horsepower unit that removes a lot of difficult sulfur from the heavy feed before it is cracked. Without the feed hydrotreater, the red refinery is placing the total Tier 3 load on the gasoline desulfurizer, which is a very low horsepower unit.

## Slide 10: What is the mix of green, yellow, and red refineries in the USA?
Notes: What is the mix of green, yellow, and red refineries in the USA? This is one of many questions that were addressed by several industry groups involved in developing the Tier 3 standard going back to 2011

## Slide 11: Green, yellow, red count
US FCC refineries count | MathPro 2011 |  | 
 | 41% |  | 
 | 24% |  | 
 | 35% |  | 
Notes: In 2011, Mathpro did a study on Tier 3 refining economics using their LP model of the US refining system. By Mathpro’s count, in 2011, we were 41% green, 24% yellow, and 35% red.

## Slide 12
US FCC refineries count | MathPro 2011 | EPA 2013 | 
 | 41% | 39% | 
 | 24% | 19% | 
 | 35% | 42% | 
Green, yellow, red count
Notes: In 2013, EPA’s study reported the same distribution. The distribution is 40/20/40. Recognizing the weaknesses of yellow and red refineries for gasoline desulfurization, these Tier 3 studies looked at every US refinery and estimated what would be required to move it up to a level for making Tier 3 gasoline.

## Slide 13: Tier 3 studies said
The US will need 82 capital investment projects
16 new builds and 66 revamps
To move red and yellow refineries toward the green category
A six-year phase in will allow for these investments
= $3 Billion in capital investment
Notes: The studies said the US needed 82 capital investment projects, consisting of 16 new builds and 66 revamps of feed pretreaters or gasoline desulfurizers, to move red and yellow refineries toward the green category. A six-year phase in was allowed by EPA for these investments to occur. BUILD It added up to $3 billion in capital investment. PAUSE. Now everything I have shown you so far was known and publicly available five years ago, in October 2014, when I was meeting with that refiner planning our Tier 3 research project. And it was accepted by the industry back then, that fact is well-documented in our reports. How much of this capital investment occurred? I have also been tracking that, and this is breaking news today I think to everyone except my clients.

## Slide 14
US FCC refineries count | MathPro 2011 | EPA 2013 | Hoekstra 2019
 | 41% | 39% | 39%
 | 24% | 19% | 22%
 | 35% | 42% | 39%
Green, yellow, red count
Notes: The answer is, nothing has changed. By my count, today we are still 40% green, 20% yellow, and 40% red. During the six-year phase in for Tier 3, there were only a handful of capital investments targeted at what is clearly the weak link, which is get sulfur out of the FCC gasoline.

## Slide 15: Breaking news -- after six years of capital investment . . .
there has been no progress in upgrading FCC process trains for Tier 3 gasoline
Notes: After six years of capital investment there has been no net progress in upgrading our FCC process trains for Tier 3 gasoline. This is one reason I disagree with the strong consensus that the industry IS ready. PAUSE. Now this green yellow red analysis is one argument, it’s a good one I think that should not be dismissed, because yellow and red refineries do face serious challenges in making 10 ppm gasoline. I am going to come back to this green-yellow-red analysis in a moment, but let's move to the next question:

## Slide 16: Tier 3 gasoline
Is the industry ready? No
What’s the problem? Octane
What’s going to happen?
Notes: Given that these investments did not occur, what’s the problem? In a word, octane. The FCC train is the main machine for producing octane barrels. And when you desulfurize FCC gasoline, you destroy some of those octane barrels.

## Slide 17: Octane loss in gasoline desulfurizer
Chart: Product sulfur ppm
| 10 | 30 | 50 | 80
current process | -6.4 | -4.1 | -3 | -2
Notes: The big issue is octane loss in the gasoline desulfurizer. While desulfurizing gasoline, there is a side reaction that destroys octane barrels that were produced in the cracker; and when we turn up the heat on the desulfurizer to remove the last traces of sulfur for tier 3, that octane loss starts going exponential. BUILD. Here is a chart of octane loss on an FCC gasoline desulfurizer. Octane loss is shown on the vertical axis, and product sulfur on the horizontal. And we want to look at this chart from right to left. As we move from right to left and lower gasoline sulfur, we are turning up the heat to desulfurize harder, and as we do that, simultaneously, by a parallel side reaction, we destroy more octane. When refiners start pushing their desulfurizers to make 10 ppm gasoline, the octane loss accellerates. We measured this curve in a 2016 field test on a commercial gasoline desulfurizer, it shows the same exponential octane loss we measured in our 2015 pilot plant studies. And we have measured it in field tests on other commercial gasoline desulfurizers. It is especially a problem in red refineries where the gasoline desulfurizer must carry the whole load for Tier 3.

## Slide 18: Octane loss in gasoline desulfurizer
Chart: Product sulfur ppm
| 10 | 30 | 50 | 80
ultimate | -1.9 | -1.2 | -0.8 | -0.5
current process | -6.4 | -4.1 | -3 | -2
expected
actual
Notes: This orange curve we call the ultimate curve because our data indicates it is about the best one can do in real life. The orange curve is also what the industry has been expecting as typical. It is not typical; it is like the best case. Our data shows US gasoline desulfurizers are much more clustered around the red curve. This difference, between the orange and red curves, BUILD between expected and actual, is unexpected octane loss that is very well documented in our reports, and it is the biggest reason I disagree with the industry consensus. This refinery, when they did their field test and measured this red curve, concluded they just cannot accept that much octane loss, and they invested some capital to move their curve up. That investment is going to pay off very nicely, and we are eager to help other refiners do that too. Some significant improvements can be achieved quickly with little or no capital investment.

## Slide 19: Hoekstra pilot plant and field tests showed
Gasoline desulfurizers in red refineries, when pushed to make 10 ppm gasoline, will lose 5 times more octane than the industry is expecting
= $ Billions/year in octane destruction
Notes: Our pilot plant and field tests showed that gasoline desulfurizers in red refineries, when pushed to make 10 ppm gasoline, will lose 5 times more octane than the industry is expecting. BUILD We estimate this additional, unexpected octane loss will add up to billions of dollars per year in octane destruction. This is the problem we forsee. PAUSE Everything I have shown you up till NOW was known by, and was paid for by, and was being used by my client group 2 years ago. That was October of 2017, when the third and last of our three annual reports on our Tier 3 research project was released. The three-year, $1.1 million dollar project ran from 2014 through 2017. I have shown only a small part of what is in those three annual reports. But let’s review three findings I have shown here that that support my contrarian view on Tier 3 readiness:

## Slide 20: Quick review: 1) Way behind schedule
Chart: US average ppm sulfur in gasoline
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
Sulfur VWA | 31.49 | 30.72 | 28.83 | 26.61 | 24.51 | 23.85 | 21.2 | 20.5 | 0 | 10 | 10
Gap
Updated June 24, 2019
Notes: First: We are way behind schedule in meeting the goal

## Slide 21
US FCC refineries count | MathPro 2011 | EPA 2013 | Hoekstra 2019
 | 41% | 39% | 39%
 | 24% | 19% | 22%
 | 35% | 42% | 39%
2) No net progress
Notes: Second: There’s been no net progress in upgrading our FCC trains for Tier 3.

## Slide 22: 3) Octane loss five times higher
Chart: Product sulfur ppm
| 10 | 30 | 50 | 80
ultimate | -1.9 | -1.2 | -0.8 | -0.5
current process | -6.4 | -4.1 | -3 | -2
expected
actual
Notes: Third octane loss is five times higher than expected when making 10 ppm gasoline.

## Slide 23: Tier 3 gasoline
Is the industry ready? No
What’s the problem? Octane
What’s going to happen? Adaptation
Notes: What is going to happen? Adaptation. Refiners are good at adapting to change. Now, we will find ways to make it work. This means adjusting operations to mitigate, or cope with, or make up for, the octane loss. But this is when the wolf sheds his disguise. The adaptations are costly.

## Slide 24: Costly adaptations
  Purchase alkylate
  Purchase toluene
  Purchase sulfur credits
  Downgrade FCC yields
  Downgrade reformer yields
  Downgrade gasoline streams
  Restrict gasoline end point
  Restrict feedstocks
  Restrict black oil recycle
Notes: Here is a partial list of adaptations. We see purchase, purchase, purchase, downgrade, downgrade, downgrade, restrict, restrict, restrict. These adaptative steps are being taken today as refiners scramble to restore their octane balance after reducing gasoline sulfur. This takes its toll on profits. Step by step, other hidden constraints and bottlenecks get exposed. The last three points on this list refer to steps that RESTRICT the ability to make high value gasoline from low value feeds. These can be especially costly . . .

## Slide 25
Fluid cat cracking (FCC) process train
Heavy feeds
Octane barrels
Notes: Because they constrain the FCC process train which is our main machine for converting low value feeds to octane barrels. In financial terms, these restrictions handcuff our ability to capture the gasoline crack spread which is how we make money. Yes we can make it work, but at what cost?

## Slide 26: Costly adaptations mean:
premium gasoline
total gasoline
octane barrels
crude flexibility
profit margin
unplanned shutdowns
credit liabilities
Notes: The cost appears in the form of lower premium gasoline, total gasoline, and octane barrel production, less crude flexibility, and profit margin, more unplanned shutdowns and credit liabilities. These consequences show up on the bottom line. My view is that the industry has not been well-aware of the size of these risks and their consequences for profits. Refiners especially should be aware, whether it effects them or their competitors. Billions of dollars/year of octane destruction is enough to move the industry’s profit needles.

## Slide 27: Don’t fall off the cliff
Notes: Don’t fall off the cliff. This picture is on the front of a flyer we’ve been passing around the industry since 2016.

## Slide 28: Move that red curve up
Chart: Product sulfur ppm
| 10 | 30 | 50 | 80
current | -6.4 | -4.1 | -3 | -2
Notes: The cliff refers to the steep red octane destruction curve I showed earlier. Octane is very valuable today, and the best solution is to not destroy the octane barrels your cracker has produced. Using our pilot plant and commercial data, and new analytical methods, we have developed a spreadsheet tool that that helps our clients see the exact chemistry happening in their desulfurizer, and the exact causes of octane loss. They can use this tool to adjust operations day-to-day to keep their curve as high as possible. It has also been used in LP studies, to evaluate and decide on capital investment options, and to help design new units. There are several capital investment options available today to move this curve up. The spreadsheet tool is included with the purchase of our second annual report on this project. It is a big step up from previously available modeling tools for this process.

## Slide 29: Predictions
Compliance will stall until 2020 √
Octane price will increase √
Tier 3 credit price will increase √
Refiners will scramble to make up lost octane √
Latent constraints and bottlenecks will surface
Tier 3 credit liabilities will accumulate
Tier 3 credit price will soar
Quarterly earnings will be affected
Readiness will be rewarded
Notes: By doing this research far in advance of the deadline, and by getting a full, detailed view of the Tier 3 issues, we have been able to make accurate predictions about how Tier 3 will play out in real life. BUILD We correctly predicted that compliance would stall until 2020, BUILD octane price would increase, BUILD Tier 3 credit price would increase BUILD and that, when the heat gets turned up, refiners will scramble to make up lost octane. Those predictions were correct. And we predicted that BUILD latent constraints and bottlenecks will surface, BUILD Tier 3 liabilities will accumulate, BUILD Tier 3 credit prices will soar, perhaps creating a RIN-like fiasco, BUILD quarterly earnings will be affected, and BUILD Good strategy, good investments, and readiness will be rewarded.

## Slide 30: The green, yellow, red analysis
Does Tier 3 require $3 billion of investment?
Or no investment?
Notes: Back to the green yellow red analysis. That analysis summarizes work done in several detailed industry studies, done between 2011 and 2013, it argues that making Tier 3 gasoline requires a green refinery, and therefore the US would need to invest $3 billion in our FCC trains. Today I have told you those investments were not made; we are still only 40% green. So this sets up the possibility of a good debate. What’s the reality? BUILD Does Tier 3 require $3 billion of capital investment in FCC trains as the industry believed 6 years ago? Or BUILD does it require no such investment, as implied by the industry’s actual capital investment decisions? There are different views on this.

## Slide 31: A good question for debate
Does making Tier 3 gasoline reliably, consistently, and profitably require a green refinery?
Notes: I would pose the debate question this way, does making Tier 3 gasoline reliably, consistently, and profitably require a green refinery? It is a good debate to have in any refinery whose profitability depends on supplying gasoline to the US market. To have a good debate, you need good data and evidence.

## Slide 32
Dozens of attachments
Notes: The best data and evidence for this debate has been gathered into our reports, which include dozens of attachments like these, 10’s of millions of dollars of the best research on this topic. We found, studied, and put to use a wealth of published research on this topic. It is included as attachments to the annual reports on our 3-year research project, to help our clients test and strengthen their Tier 3 strategy

## Slide 33: Hoekstra reports cover all the aspects
Refinery technology
Refinery economics
Refinery modeling
Octane technology
Octane economics
Octane modeling
Gasoline marketing
Gasoline regulations
Gasoline sulfur credits
Notes: Tier 3 has many aspects involving different disciplines, as shown in this list. Through 3 years of study, we became well-educated in all these aspects. Our project was not just paper studies. We gathered important new data in pilot plant, laboratory, and field tests. The reports on our project are available immediately to anyone. If you have a stake in this issue, our reports bring a broad and deep external knowledge base to supplement your own knowhow and help strengthen your Tier 3 strategy. The cost is negligible. To put the cost in perspective, the cost of our reports is equal to 1 minute’s worth of PBF Energy’s annual revenue, and only seconds of Valero’s annual revenue. So I have discussed a wolf in sheep’s clothing -- Now you are seeing an amateur salesman in engineer’s clothing.

## Slide 34: I recommend you should buy one of our reports!
Notes: I am recommending you should buy one of our reports on Tier 3 gasoline! How do you join our client group that did this three-year project? It’s very easy. You just send a purchase order for one of our reports, we deliver it immediately, and you take it from there. Nothing in our reports is confidential. You don’t need a lawyer, your standard PO terms and conditions on the internet will do. Don’t form a committee to decide whether to buy it, that will cost more than the report. Just buy one. It’s only a minute’s worth of your annual revenue and its an important topic. Take it back to the office and use this new information to help strengthen your Tier 3 strategy. And I will finish by quoting a true professional salesman:

## Slide 35: What have you got to lose?
Notes: What have you got to lose?

## Slide 36: Thanks for your attention!
George Hoekstra
OPIS Fuels and Octane Forum Oct. 24, 2019
george.hoekstra@hoekstratrading.com +1 630 330-8159
Tier 3 video -- 10 nuggets in 4 minutes
Tier 3 gasoline – A wolf in sheep’s clothing?
Notes: Thanks a lot for your attention.